## Slide 1
Product Knowledge Pricebook

## Slide 2: Traditional Shower Drain

## Slide 3: Linear Drains
Slope the floor in one direction towards the drain
Use large format tile, stone slab or solid surface material
Create a barrier-free or curbless shower
Drain is now a design element

## Slide 4: How Do I Choose?
Which one do I like?
Which one do I need?

## Slide 5: Decorative Top Grates
Finish Options Available
Satin Stainless Steel
Polished Stainless Steel
Oil Rubbed Bronze
Matte White
Matte Black

## Slide 6: Traditional Waterproofing
Lead Pan/Copper Pan
PVC Vinyl
Rubber Liner (Chloraloy™)
Hot Mop
Notes: These methods require multiple levels of installation, skill set, and limited square footage. They also use a clamp down method water in/water out drain system.
The traditional method for installing tiled shower assemblies begins with the installation of a mortar bed that is sloped to the weep holes in the drain. A waterproofing membrane, typically referred to as a pan liner, is subsequently placed over this "pre-slope" and clamped into the drain. Pan liners may consist of metals such as lead and copper or plastics such as polyvinyl chloride (PVC) and chlorinated polyethylene (CPE). Some regions of the country also employ hot mop systems that involve applying layers of asphalt and roofing felt to build up a pan liner. Pan liners are carried up to a height of at least 3" above the finished height of the curb, and must not be penetrated by any fasteners. Pan liners are not designed to allow for the direct application of ceramic or stone tile. Thus, a mortar bed must be installed to provide load distribution and a bonding surface for the floor tile. Crushed stone or tile is placed around the weep holes of the drain to prevent blockage before installing the mortar bed. Most wall assemblies incorporate 4-mil polyethylene or roofing felt placed behind the tile substrate (i.e., floated mortar or backerboard panels) and lapped over the pan liner.

## Slide 7: Site Sizable Linear Drain Systems
Modify length of grate and channel on-site to exact specifications
Place outlet anywhere along channel run
Channel in Stainless Steel or PVC
Neutral pitch channel
Components can be combined for form any length.

## Slide 8: Site Sizeable Clamping Flange – PVC Channel, Against the Wall

## Slide 9: Site Sizeable Clamping Flange – All Stainless Channel, Against the Wall

## Slide 10: Fixed Length Linear Drain Systems
Fixed Length grate and channel
Set center outlet location
Pre-pitched channel
Stainless steel grate and channel l
Challenges in perfect wall-to-wall installation
Custom sizing available

## Slide 11: Fixed Length Clamping Flange – Straight Edge Channel, Zero-Threshold

## Slide 12: Modern Waterproofing No-Hub Connection with Coupling
Fabric Sheet
Schluter Kerdi System, Nobel
Adheres to substrate with thinset
Allows for direct tile application—huge floor height savings.
Liquid Membrane
Laticrete Hydro Ban, Red Guard
Paint-on or roll onto the substrate
Allows for direct tile application—huge floor height savings.

## Slide 13: Fixed Length Direct Connect – Flanged Channel, Against the Wall

## Slide 14: Video

## Slide 15: Recommended Drain Placement

## Slide 16: Recommended Drain Placement

## Slide 17: Recommended Drain Placement

## Slide 18: Recommended Drain Placement

## Slide 19: Outdoor Architectural Trench Drains
Outdoor Installations

## Slide 20: Storm Drainage & Landscape

## Slide 21: Patios & Balconies

## Slide 22: Pricebook